[First page]

Numerical Analysis of Flow Behavior in Meniscus Region of

Viscoelastic Dip Coating Flows

# YAMAMOTO Takehiro a,*, NOJIMA Naosuke b, MORI Noriyasu a

(Family name should be written in CAPITAL characters.)

## a Graduate School of Engineering, Osaka University, 2-1 Yamadaoka, Suita, Osaka 565-0871, Japan

b Faculty of Education, Shiga University, 2-5-1 Hiratsu, Otsu, Shiga 520-0862, Japan

#### Received 13 January 2005; accepted for publication 28 April 2005

* Corresponding author: E-mail: take@mech.eng.osaka-u.ac.jp, Tel: +81-6879-7309, Fax: +81-6-6879-7308

[Second page]

### Abstract  (double space)

Flow behavior in a meniscus region in viscoelastic dip coating flows was numerically analyzed using a finite element method. The Phan-Thien Tanner (PTT) model was used as a constitutive equation. The problem considered was a flow around a rod withdrawn from a viscoelastic liquid in a cylindrical reservoir. Both the velocity and stress fields were analyzed for three kinds of PTT fluids that were different in elongational properties. The profile of meniscus formed between the moving rod and the liquid level became thinner at higher withdrawal velocity and for a fluid having stronger stretch-thickening property of elongational viscosity.

Key Words: Dip coating flow, Viscoelastic fluid, Numerical simulation, Phan-Thien Tanner model, Meniscus

[Third page]

1. Introduction

(double space)

Coating flows are widely used in the industrial processing to cover a large area of surface of products and various kinds of coating processes exist [1, 2]. In the dip coating, a substrate is withdrawn from a reservoir of coating liquid and then the substrate is coated by the coating material. For a special application, the dip coating flow is also utilized for manufacturing capsules. Coating film thickness is an important subject and has been theoretically studied in Newtonian cases, and the theoretical predictions were compared to experimental results [38].

2. Basic equations

Basic equations include the equation of continuity, the equation of motion, and a constitutive equation. The equation of continuity (1) and the equation of motion (2) are denoted as follows:

,		   (1)

(2)

(size of the variables is 10pt, size of superscript or subscript is 6pt)

5. Concluding remarks

References

- Ruschak KJ (1985) Ann Rev Fluid Mech, 17, 65-77

- Tallmadge JA, Gutfinger C (1967) Ind Eng Chem, 59, 18-30

- Alexander LF (1998) “Polymer Science”, pp135-140, John Willey Sons, New York

- Homsy GM, Geyling FT (1977) AIChE J, 23, 587-600

[5] Nishi Kikai Co., Ltd (2010) Japansese Patent 19530313

Figure captions

Fig.1 Schematic diagram of a circular contraction and Observation planes.

Table captions

Table 1 Flow visualization conditions of the 0.2 and 0.5wt%PAA solutions.

Fig.1